## Slide 1: Optimizing The Contra-Directional Couplers Models March, 2019
Mustafa Hammood,
The University of British Columbia

## Slide 2: Approaches
Full-length 3D FDTD Simulation
  Slowest: Time and resources consuming, high risk of divergence
  Accurate simulation, if your simulation converges…
EME Propagation Simulation
  Fast (er?)
  Difficult to simulate non-uniform grating profiles (not impossible)
  Difficult to simulate unconventional perturbations (i.e. sinusoidal)
  Accurate within contra-coupling wavelengths
Analytical: Coupled-mode Theory + Transfer Matrix Method
  Fastest
  Most accurate, can model every profile, and every band (self+contra)
  Requires prior knowledge of device parameters:
    Waveguides system modes
    Coupling coefficients / Kappa

## Slide 3: Coupling Coefficient / Kappa
Dependent on the waveguides geometry and structure of the perturbation gratings (strength/shape)
Determines the bandwidth and reflectivity of the device
The key parameter that sets coupled-mode theory model to work.

## Slide 4: How to find Kappa? Analytically
Can be modelled analytically using:
  Accurate for small perturbations
  Easily implemented for simple
  perturbations
  Difficult to find the Fourier-expansion term (Δε) for unconventional perturbations shapes (ex: sinusoidal or litho. smoothed corrugations)
(a) (c) (b)

## Slide 5: How to find Kappa? Experimentally, extracted from a response
Can be extracted from a device response/modelled experimentally using:
Given any device response (either experimental/simulation) we can find Kappa, assuming a waveguide system (to find ng).
Several means to extract from experimental data:
  FWMM Method (Robi 2017)*
  Nulls method*
* Not always applicable

## Slide 6: How to find Kappa? Simulation using Bloch boundary band-structure
Using an infinite length, Bloch boundary band-structure simulation, we can calculate the bandwidth and wavelength of the system’s forbidden bands
  Self-Bragg bands at Kx = 0.5 – labelled (A)
  Contra bands at unknown Kx – labelled (B)
Uncertainty of contra wavevector (Kx) means we have to sweep a large range to find where the contra-coupling forbidden band occurs. This is time and resource consuming. Below plot is generated from 20 points

## Slide 7: How to find Kappa? Simulation using Bloch boundary band-structure
Can we do better, simulation time and resources wise? Interpolate the system’s forbidden bands?
Can 2 simulations at two wave-vectors to predict the location of the contra-bandgap?
 | Kx | Bandwidth (nm)
Actual | 0.4796 | 5.32
Predicted | 0.4794 | 5.88
Test case:
Error <10%

## Slide 8: How to find Kappa? Even faster? MODE EME Simulation
Simulate a single periodic contra-DC cell in EME
Generate the uniform profile response
Extract kappa from the response using the nulls method
Feed the kappa into coupled-mode theory, transfer matrix apodized model

## Slide 9: What’s new?
Fully automated flow in Python – no need for a MATLAB engine for coupled-mode theory or the setup of any 3rd party tools (other than Lumerical)
Generates an S-parameter file (.dat) for circuit simulations
Dual polarizations: TE-TM, compact model includes two-modes support
Two new approaches to find the bandgap and Kappa – reduce FDTD simulation time from more than 5 hours to an improved, to less than a minutes. This was the simulation flow bottleneck.
Accurately predicts and simulates the waveguide’s self-reflection
Higher level of abstraction

## Slide 10: How to? Define physical parameters and simulation parameters
Optional
Feed in the design parameters
  Let the script run!

## Slide 11: Further improvements can be done on…
Parameterized sidewall angle
Model sensitivity to process variations and corner analysis
  Conclusion: bandwidth is somewhat stable, central wavelength not quite.
Segmented kappa: Wavelength-dependent coupling coefficient
Chart: Sensitivity to height variations (H)
| 215 | 220 | 225
 | 1530.77 | 1533.91 | 1537.16
series2 | 6.3362 | 6.5312 | 6.7181
Chart: Sensitivity to sidewall angle variations (θ)
| 90 | 85 | 80 | 75
 | 1530.77 | 1533.91 | 1537.16
series2 | 6.3362 | 6.5312 | 6.7181
𝛿(λ0)/ 𝛿(θ) = 0.63 nm/degree
𝛿(λ0)/ 𝛿(H) = 0.7 nm/nm

## Slide 12: Contributors
Wei Shi
Mustafa Hammood
Jonathan St-Yves
Simon Belanger
Dominique Charron
Han Yun
Xu Wang
Ajay Mistry
Stephen Lin